## Slide 1
Lab Book 1.0. Waveguides
Student:

## Slide 2: Instructions General
SCRIPTS
From GitHub 
  Fork the repo: https://github.com/cccanvas-upv/cifoin-lab1.git
  Clone the repo using VSCode
Run the Jupyter Notebook:
  WAVEGUIDES_Student.ipynb
h
(height)
/
thickness
W (width)
Core
Cladding
W (width)
Core
Cladding
Slab
h_slab
h_core
shallow waveguide
deep waveguide

## Slide 3: Learning outcome #1 – Effective index of a waveguide
INSTRUCTOR:
Present Python and GDSFactory: materials, output, results.
Explain how to run a simulation for a particular cross-section.
Showcase how to change between shallow and deep waveguide.
Describe how to change the wavelength and width for the waveguide analysis.
Describe the outputs.
ALL EXAMPLE #1: waveguide width 1.2 µm, deep wvg, wavelength start and end same 1.55 µm  all ”Run”
ALL: Follow instructor, that will show how to 1) plot mode, 2) explore the results (neff …)
Document all your results (neff, plot fields of different modes, comparison between different polarizations…)

## Slide 4: Learning outcome #2 – Wavelength behavior Wavelength 1.5-1.6 µm (step 0.01 µm) – width 1.2 µm
Comment results (neff changes this way with wavelength, comparison between different waveguide cross-sections …etc)
shallow waveguide
Paste plot here
deep waveguide
Paste plot here
slab = 150nm

## Slide 5: Learning outcome #3 – Width dependence Width 0.6 - 1.6 µm (step 0.1 µm) – Wavelength 1.55 µm
Comment results (neff changes this way with width, polarization behavior, etc…)
deep waveguide
Paste plot here

## Slide 6: Learning outcome #4 – Waveguide compact model - Find the compact models of the following waveguides: Deep waveguide, h=300nm, w=1.2um - Shallow waveguide, core h=300nm, slab h=150 nm, w = 1.2um
Find the second-degree polynomial coefficients and relate them with the group index and the dispersion parameter.
Comment on the results found for the TE0 and TM0 for both deep and shallow waveguides.
deep waveguide
neff_TE0 vs with the second-degree polynomial fit
& neff_TM0 vs with the second-degree polynomial fit
shallow waveguide
neff_TE0 vs with the second-degree polynomial fit
& neff_TM0 vs with the second-degree polynomial fit
slab: 150nm

## Slide 7: Learning outcome #5 – Bend waveguide radius vs. loss – deep Find neff_TE0 for wvl 1.55 µm, width 1.2 µm for R=25,50,75,100, 125,150 µm
Comment results, which is the safe radius?, consider safe means less than 0.1 dB/90º.
deep waveguide
Paste Total Loss (dB/90º) vs R & neff_TE0 vs R

## Slide 8: Thank you